## Slide 1
Course 1: Digital Farming and Precision Agriculture
M1: IoT in use – Precision Agriculture
www.smartskillsproject.eu

## Slide 2
Understand…
Identify…
Explore…
…the use of sensors to measure soil moisture, temperature, movement, and more.
…key components of control systems, including sensors, controllers, and actuators.
…how GIS supports decision-making through spatial analysis and mapping.
This module explores how data and modern technologies are transforming agriculture. Learners will gain insight into how the Internet of Things (IoT) enables real-time data collection from sensors in fields, greenhouses, and on animals—measuring soil moisture, temperature, movement, and more. The module covers data analysis techniques that help visualise and interpret this information to optimise processes. It also introduces Geographic Information Systems (GIS), which allow spatial analysis and mapping of yields, vegetation, and pest presence to support decision-making.
What will you learn?

## Slide 3
01
IoT in agriculture
02
Precision agriculture
03
IoT in use – Case Study
04
Further development, criticism, trend
contents
05
Lets Practice

## Slide 4
IoT IN AGRICULTURE
01

## Slide 5
IoT in agriculture/ smart agriculture
Management systems - LPIS administration automation, "employee tracking"
Security - Buildings, hay straw fires, floods, animals...
Sensors - weather station
Robotisation
Precision farming - Plant production
  Fields, orchards, greenhouses
Animal production
Forestry
Water management

## Slide 6
IoT in Agriculture/ The Smart Future of Farming
(Source: Farooq, M.S.; Riaz, S.; Abid, A.; Umer, T.; Zikria, Y.B. Role of IoT Technology in Agriculture: A Systematic Literature Review. Electronics 2020, 9, 319. https://doi.org/10.3390/electronics9020319
IoT Technology in Agriculture (see the graph)
provides a comprehensive overview of how IoT is transforming agriculture. Here are the key points:
The Internet of Things (IoT) is revolutionising agriculture: sensors monitor the soil, greenhouses are controlled automatically, and animals wear devices that monitor their health.
In the 67 analyzed studies (2006–2019), IoT is most often applied in:
Precision agriculture - e.g. targeted irrigation or fertilization
Animal monitoring - health, movement, localization
Greenhouse automation - climate control without human intervention
IoT helps save water, increase yields, and make work easier - even remotely.

## Slide 7
PRECISION AGRICULTURE
02

## Slide 8
Precision agriculture
Precision agriculture began to take shape in the 1980s. The main goal of early research in this field was to develop a Decision Support System (DSS) for comprehensive farm management. This system aimed to:
Optimize the return on agricultural inputs (e.g., seeds, fertilizers, water)
Conserve natural resources by applying them only where and when needed
Improve efficiency and sustainability through data-driven decisions
This foundational idea laid the groundwork for today’s smart farming technologies, including IoT, GIS, and automation.

## Slide 9
Selected areas - plant production
Automatic control of precision sowing according to sowing map
Automatic regulation of fertilization dosage based on fertilization map
Automatic regulation of row seeding based on seeding map
Automatic setting of fertilization dosage based on current state of vegetation
Autonomous guiding of agricultural machinery
Creating application maps for fertilization
Creation of maps of physical and chemical properties of soil
Guided drive of tractors and agricultural machinery on parcel
Guided drive of tractors and agricultural machinery on parcel with 2 cm accuracy
Mapping harvest yields of root crops
Mapping the quality of harvested crops during harvesting of cereals and forage crops

## Slide 10
Selected areas - plant production (continued)
Monitoring of outputs from cereal and oilseed harvests
Monitoring of wildlife animals on farmland and in forests using drones
Telematics for tractors and other agricultural machinery
Use of unmanned vehicles for the management of crop production
Using field robots in fruit and vegetable production
Using satellite imagery for management of crop production
Utilization of drones for application of plant protection mixture
Variable application of plant protection products according to the map of occurrence of harmful factors
Variable soil treatment

## Slide 11
Maps / Mapping
revenues
fertilisation
vegetation condition
soil properties
plot profile

## Slide 12
Maps / Mapping – Real-Time Kinematic (RTK) Positioning
Real-Time Kinematic (RTK) positioning is a satellite navigation technique used to enhance the precision of GPS signals. It is widely used in precision agriculture for tasks that require high spatial accuracy.
Key features include:
Error Correction: RTK corrects signal errors from standard GPS using data from a nearby base station.
High Accuracy: Achieves positioning accuracy of 2–5 cm, essential for tasks like automated steering, planting, and spraying.
Real-Time Data: Provides immediate corrections, allowing for precise operations in the field without delays.
Mapping Applications: Enables the creation of detailed field maps, including yield maps, soil property maps, and application maps.
RTK technology is a cornerstone of modern precision farming, enabling farmers to work more efficiently and reduce input waste.

## Slide 13
Remote Sensing Types
Active - light
Passive artificial sources
Drones
Satellites
  ESA's Copernicus programme
  Sentinel satellite - EU images freely available
  atmospheric monitoring (air quality, emissions, ozone layer)
    marine environment monitoring
    water monitoring
    soil monitoring
    vegetation monitoring
    climate change monitoring

## Slide 14
Remote Sensing Tool
What is CropSat and How Does It Work
CropSat is a free online tool for monitoring the condition of agricultural crops using satellite imagery.
Uses satellite data from the European Sentinel missions (Copernicus programme)
Supports both RGB (visible light) and CIR (colour-infrared) imagery
Displays vegetation indices (e.g. NDVI) to assess crop development
It enables users to:
Track crop growth over time
Optimise fertilisation and irrigation
Compare fields across seasons and locations

## Slide 15
Remote Sensing Tool
CropSat for Security and Crisis Management
Security & Monitoring:
Detects drought, deforestation, and land degradation
Identifies unusual land use changes or illegal activities
Crisis Management:
Evaluates impact of natural disasters (fires, floods, droughts)
Supports decision-making for aid distribution and recovery planning
CropSat = a tool for farmers, policymakers, and landscape protection alike.

## Slide 16
NDVI (Normalized Difference Vegetation Index)
NDVI (Normalized Difference Vegetation Index) is a numerical indicator used to assess the health and density of vegetation using satellite or aerial imagery. It is calculated using the difference between near-infrared (NIR) and red (RED) light reflectance
vegetation recognition
determination of vegetation health (amount of biomass)
amount of chlorophyll
CWSI (crop water stress index)

## Slide 17
Precision Agriculture – Farm Management
Farm management in precision agriculture involves the integration of digital tools and data-driven decision-making to optimise agricultural operations. By using technologies such as IoT sensors, GPS, and farm management software, farmers can monitor and control various aspects of their production in real time.
Key components include:
Data collection from fields, machinery, and livestock
Dashboarding for visualising performance indicators
Automated reporting for compliance and planning
Decision support systems (DSS) to guide actions like irrigation, fertilization, and harvesting

## Slide 18
Precision Agriculture - Robotisation
Robotisation in precision agriculture refers to the use of autonomous and semi-autonomous machines to perform agricultural tasks with high accuracy and efficiency. These technologies reduce the need for manual labour and enable 24/7 operations under various conditions.
At all stages
  Breeding
  Field preparation
  Betting
  Fertilisation
  Harvesting
  …

## Slide 19
Precision Agriculture - Greenhouses
Greenhouses in precision agriculture use advanced technologies to create controlled environments that optimise plant growth and resource efficiency. IoT sensors and automation systems monitor and regulate key variables such as temperature, humidity, light, and nutrient levels.
Closed-loop systems
Hydroponic and aeroponic systems
Automated climate control
Remote monitoring and alerts
AI-driven optimisation

## Slide 20
More information about Digital Farming
 Why Digital Farming is Important For Farmers? Digital Agriculture
| Discover Agriculture
Digital Farming

## Slide 21
IoT IN USE – CASE STUDY
03

## Slide 22
Case Study: Senosec.cz: Protecting Wildlife During Grass Mowing
During grass mowing, young deer and other small animals hide in the tall grass, often resulting in fatal injuries. The Senosec.cz system uses thermal imaging drones and field sensors to scan the area before mowing. The data is visualised on GIS maps, allowing farmers to avoid harming hidden animals. The solution has reduced animal casualties and improved the public image of farming practices. However, it also presents challenges, including the cost of drones, the need for trained personnel, and privacy concerns related to image data.
Problem: Hidden animals injured or killed during mowing
IoT-based solution: Thermal drones and field sensors detect animals
GIS mapping for precise localisation
Impact: Reduced wildlife mortality, improved farm ethics
Challenges: Drone operation, equipment cost, data privacy (GDPR)

## Slide 23
Case Study: Vcelstva.cz: Remote Beehive Monitoring
Beehive health is critical for pollination and honey production. Vcelstva.cz enables remote monitoring through smart hive scales and temperature/humidity sensors. The data is transmitted via LoRaWAN to a web interface, allowing beekeepers to check hive conditions anytime. This reduces the need for physical checks and improves the response to issues such as swarming or disease. Challenges include maintaining connectivity in remote areas, ensuring accurate calibration, and protecting sensitive data.
Problem: Hidden animals injured or killed during mowing
IoT-based solution: Thermal drones and field sensors detect animals
GIS mapping for precise localization
Impact: Reduced wildlife mortality, improved farm ethics
Challenges: Drone operation, equipment cost, data privacy (GDPR)

## Slide 24
Case Study: PtaciOnline.cz: Bird Tracking and Research
The PtaciOnline.cz project focuses on tracking the migration of protected bird species. Small GPS devices attached to the birds collect position and activity data, transmitted via GPRS. This information helps scientists understand flight paths and behavioral patterns, supporting conservation programs. However, the devices must be lightweight to avoid harming the birds, battery life is limited, and ethical questions may arise around animal tagging.
Problem: Need to study bird migration and behaviour
IoT solution: GPS collars with GPRS and motion sensors
Real-time data for research and conservation
Benefits: Accurate migration maps, wildlife protection
Challenges: Battery life, device weight, ethical concerns

## Slide 25
Case Study: PtaciOnline.cz: Bird Tracking and Research
FARMBOT is an open-source agricultural robot designed for small-scale automated farming, such as home gardens or research plots. It operates like a CNC machine over a raised bed, performing tasks like sowing seeds, watering plants based on moisture levels, and even removing weeds. FARMBOT connects to a cloud-based platform and can be controlled from a web app. It’s an excellent example of precision agriculture at the micro level—especially for educational use or demonstration purposes. However, its use is limited to small plots and requires internet connectivity and basic technical skills for setup and maintenance.
Problem: Time-consuming manual gardening and small-scale crop production
Solution: Open-source CNC farming robot – fully automated plant care
Functions: Seeding, watering, weeding, soil moisture sensing
Benefits: Fully autonomous growing, ideal for education and urban farming
Challenges: Limited scalability, needs internet and technical skills

## Slide 26
FURTHER DEVELOPMENT, CRITICISM, TRENDS
04

## Slide 27
Criticism of IoT
While IoT offers many benefits in agriculture, it also faces several criticisms and challenges:
Data Overload: Large volumes of data can be difficult to manage, analyze, and interpret effectively.
Incompatibility: Devices and platforms from different manufacturers may not work well together, limiting integration.
Privacy Concerns: Use of cameras, GPS, and tracking tools raises ethical and legal issues (e.g., GDPR).
Security Risks: Many IoT devices lack proper cybersecurity, making them vulnerable to hacking or data breaches.
High Costs: Initial investment in IoT infrastructure and training can be expensive for small farms.
Dependence on Connectivity: Reliable internet access is essential, which may be limited in rural areas.
Job Displacement: Automation may reduce the need for manual labor, raising concerns about employment.

## Slide 28
IoT Trends
Trends in IoT use of AI/ML
Development of wireless technologies (5G, NB)
Power supply development
  battery
  alternative
Healthcare
Agriculture, biology
Safety
Transport/Cities
Energy saving

## Slide 29
LET’S PRACTICE
05

## Slide 30
Learner Exercise:
Practical Activity: "Find a Smart Solution"
Research a real-world example of an IoT-based technology used in agriculture (e.g., soil moisture sensor, smart irrigation system, livestock tracking).
Task: Describe how the technology works, what benefits it brings, and what challenges may arise in its use. Length: 100–150 words.
Optional: Attach a video or image demonstrating the system.

## Slide 31
Discussion Prompt:
Which areas of agriculture do you think should be digitalized next? What ethical, technical, or organisational barriers might prevent wider adoption of IoT on typical farms?
Purpose:
Connect theory with practice, promote critical thinking, and assess the
real-world impact of digitalization in agriculture.
Group Exercise:

## Slide 32
You have finished the first module of Course 1! Keep going on this learning journey.
In the next module you will learn about IoT devices, sensors, actuators, converters.
Well done!
www.smartskillsproject.eu
Follow our journey