## Slide 1
M1: Fundamentals of Smart Irrigation
www.smartskillsproject.eu
Course 2: Smart Irrigation and Fertilisation

## Slide 2
Understand…
Identify…
Explain…
…the importance of water efficiency in agriculture and basic water-saving farming practices.
…differences in the functioning and use of irrigation systems.
…what role IoT plays in irrigation management.
This module aims to provide you with a comprehensive introduction to the basics of smart irrigation, which is the modern method of managing water in agriculture. You will learn how important it is to save water in today's world and how agriculture can be more environmentally friendly and efficient. You will learn the differences between drip and sprinkler irrigation systems and understand how IoT (Internet of Things) technologies help in automatic and precise water delivery to plants. This material will help you understand how science, technology and agriculture are joining forces to create a more environmentally friendly future.
What will you learn?

## Slide 3
01
Water-efficient farming practices
02
Drip and sprinkler irrigation systems
03
Role of IoT in irrigation management
04
Let’s Practice!
Module 1 introduces the essentials of water-efficient farming, comparing drip & sprinkler irrigation systems while highlighting how IoT technologies enable precise, data-driven water management. Learners explore how smart irrigation boosts yields, reduces waste, and supports sustainable agriculture in the face of climate change.
contents
This license enables reusers to distribute, remix, adapt, and build upon the material in any medium or format, so long as attribution is given to the creator. The license allows for commercial use. CC BY includes the following elements:
BY: credit must be given to the creator.
This project has been funded with support from the European Commission. The author is solely responsible for this publication (communication) and the Commission accepts no responsibility for any use may be made of the information contained therein. In compliance of the new GDPR framework, please note that the Partnership will only process your personal data in the sole interest and purpose of the project and without any prejudice to your rights.

## Slide 4
WATER-EFFICIENT FARMING PRACTICES
01

## Slide 5
The importance of water in agriculture
Water is the main resource for plant and animal production. Climate change is generating fluctuations in temperature and rainfall, forcing farmers to rethink their farming and livestock strategies in conditions of periodic water shortages.

## Slide 6
Water-saving practices
Monitoring soil moisture – the use of sensors allows to precisely determine the water needs of plants.
Efficient irrigation – drip irrigation systems and precision sprinklers to reduce water loss. Leveraging IoT and automation – Intelligent irrigation control optimizes water consumption based on real-time data. Drought-resistant crops – a selection of plants adapted to water scarcity conditions.

## Slide 7
DRIP & SPRINKLER IRRIGATION SYSTEMS
02

## Slide 8
Drip irrigation and sprinkler systems
Smart irrigation is a key element of modern agriculture, enabling water savings, optimization of consumption and ensuring the right conditions for plant growth. One of the most effective solutions is a drip irrigation system, which supplies water directly to the roots of plants, minimizing water losses associated with evaporation or surface runoff.

## Slide 9
Drip systems
They are one of the most effective ways of irrigation. They consist in supplying water directly to the root zone of plants using a network of pipes and drippers. This ensures that water is used as efficiently as possible, minimizing losses and providing optimal growth conditions for plants. Drip systems can be automated with soil moisture sensors and controllers, allowing for precise irrigation management.

## Slide 10
Sprinklers
Water is distributed to the surface of the soil in the form of tiny droplets that mimic natural rain. The sprinklers can be programmed to work at specific times and adapted to different types of crops. They are particularly useful for irrigating lawns, pastures and large agricultural areas.

## Slide 11
Factor | Drip irrigation | Sprinklers
Water efficiency | Very high (90-95%) | Average (60-80%)
Installation cost | Medium/High | Medium
Use | Row crops, orchards, greenhouses | Lawns, farmlands
Impact on soil erosion | Minimal | Possible erosion
Automation capability | Yes | Yes
Comparison of efficiency

## Slide 12
03
ROLE OF IOT IN IRRIGATION MANAGEMENT

## Slide 13
The role of IoT in irrigation management
Combined with Internet of Things (IoT) technology, these systems become even more efficient. With soil moisture sensors, temperature sensors, as well as integration with weather data, farmers can monitor the condition of the soil in real time and irrigate only when necessary. In this way, water consumption is closely matched to the current needs of the plants, which results in financial savings and contributes to the sustainable development of agriculture

## Slide 14
Key elements of a smart irrigation system:
Soil moisture sensors – measure the current water level in the soil and send the data to the system. Weather Sensors – Forecast rain and evaporation, helping you optimize your watering schedule. Controllers and mobile apps – allow farmers to remotely control irrigation based on the data collected. AI and Big Data systems – analyze crop history and climate forecasts to further optimize water use.

## Slide 15
How does an IoT irrigation system work?
An IoT-based irrigation system typically consists of several components: sensors, a control system (e.g., a smartphone or computer), an irrigation system (e.g., drip irrigation), and access to weather data. Sensors installed in the soil measure moisture levels and temperature and then transmit this data to the control system. If the soil moisture drops below a certain level, the system starts irrigation.

## Slide 16
Benefits of using IoT in irrigation
Precision and savings in water management
Enhanced growth cycles
Sustainable development
Increase in yields
Based on accurate sensor data, the irrigation system delivers water only when it is needed. Less water consumption leads to cost savings.
Automation can also help in better manage plants growth cycles, making it possible to achieve maximum yields at every stage of their development
Thanks to this technology, it is possible to manage resources more efficiently, which allows to minimize the negative impact on the environment.
Optimal water supply to plants translates into better growing conditions and higher yields. Plants watered in a precise way are healthier and more resistant to environmental stresses, such as drought or excess water.

## Slide 17
How Smart Irrigation Works
Watch the video and learn the basics of how an IoT-based irrigation system works properly
IoT smart water irrigation monitoring system Automatic Plant Watering System Blynk cloud

## Slide 18
Be Inspired: Practical application of drip irrigation on the farm of Szymon Leszczyński:
8ha of potato plantations 100% increase in yield in the first year of application reducing disease pressure Improved crop quality
Watch the video and pay attention to:
- Advantages and disadvantages of the droplet system - what is necessary when setting up and using the system
Nawadnianie kropelkowe w uprawie ziemniaka | RPZ #14 - YouTube

## Slide 19
04
LET’S PRACTICE

## Slide 20
Learner exercise: Scenario
You plan to grow cucumbers on the ground. By analyzing climatic conditions and weather forecasts, you find that the amount of rainfall may not be sufficient to meet the water needs of cucumbers. What will you do?
Answer B
Answer A
Invests in a sprinkler system to ensure the right amount of water
I don't do anything. I hope that the yields will be high anyway
I install a drip irrigation system throughout the field
Answer C

## Slide 21
Feedback on answers
Option A
Option C
Option B
Sprinklers will provide the right amount of water to your crop. But remember! Cucumbers do not like moisture on the leaves, as it increases the risk of downy mildew and other fungal diseases
The least expensive idea, but is it profitable? It may turn out that you will not get the right amount and crops to cover the costs.
Great choice. You will provide the cucumbers enough water and reduce the possibility of fungal diseases

## Slide 22
GREAT JOB!
In this module, you have learned about the different ways of irrigation and their advantages and disadvantages. In the next module, you will learn more about IoT supporting smart irrigation systems.

## Slide 23
Follow our journey
www.smartskills.eu